## Slide 1
Dillingham Pathogens
Water Quality Monitoring Project
2022-2023
Alaska Department of Environmental Conservation
With data support from Alaska Water Laboratories, LLC

## Slide 2: Introductions
Laura Eldred
Section Manager, Nonpoint Source Water Quality
Alaska Department of Environmental Conservation
Phone: (907) 376-1855
Email: laura.eldred@alaska.gov
Mary Inovejas
Environmental Program Specialist
Alaska Dept. of Environmental Conservation
Nonpoint Source Water Quality
Phone: (907) 269-7518 Email: mary.inovejas@alaska.gov
Mary Curry
Lab Director and Manager
Alaska Water Laboratories, LLC
Wasilla, AK

## Slide 3: Project Background & Goals
Objectives:
Monitor recreational beaches for fecal indicator bacteria
Identify possible bacteria sources through Microbial Source Tracking (MST) – a type of DNA speciation
Background:
Sample collection occurred between May and August during the summers of 2022 and 2023
Alaska Water Laboratories collected near-shore water samples from 3 Dillingham beaches
Pathogen monitoring was conducted in Dillingham in 2006, 2008, 2009, and 2010

## Slide 4: What are we monitoring for?
Although these pathogens are generally not harmful themselves, they indicate the possible presence of disease-causing bacteria, viruses, and protozoans that also live in the digestive systems of humans and other warm-blooded animals.
The presence of fecal coliform and enterococci in a waterbody suggests that harmful bacteria might also be present, posing a health risk.
Enterococci
Fecal coliform

## Slide 5: Water Quality Criteria
Recreation (Primary Contact)
In a 30-day period, the geometric mean of samples may not exceed 35 enterococci CFU/100 ml
Not more than 10% of the samples may exceed a statistical threshold value (STV) of 130 enterococci CFU/100 ml.
Harvesting Raw Mollusks or Other Raw Aquatic Live for Consumption
The geometric mean of samples may not exceed 14 fecal coliform/100 ml
Not more than 10% of the samples may exceed 31 CFU per 100 ml for a membrane filtration test
*18 AAC 70 WATER QUALITY STANDARDS
&

## Slide 7
Scandinavian Beach
Snag Point
2022
2023
Kanakanak Beach

## Slide 8
Results from 2022 enterococci analyses, all sites.
Results from 2023 enterococci analyses, all sites.

## Slide 9
2022 and 2023 geometric mean results for enterococci, all sites.

## Slide 10
Results from 2022 fecal coliform analyses, all sites.
Results from 2023 fecal coliform analyses, all sites.

## Slide 11
2022 and 2023 geometric mean results for fecal coliform, all sites.

## Slide 12
2022 Microbial Source Tracking (MST) Results

## Slide 13
2023 Microbial Source Tracking (MST) Results

## Slide 14
Conclusion
The final results indicate varying bacteria levels during both years, with no persistent human-caused bacteria pollution. The primary suspected source is naturally occurring from gulls.
Please follow safe food handling recommendations and cook seafood to a minimum internal temperature of 145 degrees Fahrenheit to destroy any bacteria. Note that freezing alone does not kill pathogens.

## Slide 15: For more information on….
State of Alaska Water Quality Standards, visit:
https://dec.alaska.gov/water/water-quality/standards/
2022-2023 Dillingham Pathogens Monitoring Final Report, visit:
https://dec.alaska.gov/water/water-quality/nonpoint-source-control/water-quality-resources/reports
Food safety and sanitation, visit:
https://dec.alaska.gov/eh/fss/resources-printable/
Dillingham Pathogen Monitoring Project Highlights, visit:
https://dec.alaska.gov/water/water-quality/project-highlights-newsletters

## Slide 16: Thank you!
Questions?